## Slide 1
Citicorp Center Wind Loading Crisis Simulation
OR 750: Reliability, Safety, and Risk | George Mason University | ASCE 7-22 / AISC 360-22
Building Parameters
Height:
915 ft (279 m)
Plan:
157 x 157 ft (square)
Stories:
59 (50 above stilts)
Stilt Height:
114 ft (9 stories)
Column Placement:
Mid-face (NOT corners)
Corner Cantilever:
72 ft
Total Steel:
24,000 short tons
Fundamental Period:
6.5 sec
TMD Mass:
400 tons (floor 63)
Structural System
Unique Design:
• 4 columns at face midpoints (not corners)
• St. Peter's Church below SW corner
• 72 ft cantilevers at all corners
• 6 tiers of chevron (V) bracing (48 braces)
• 2-story W-pattern transfer truss at stilt top
• 400-ton tuned mass damper (TMD)
The Crisis (1978):
• Original spec: CJP groove welds
• Bethlehem Steel substituted A325 bolts
• Bolts sized for perpendicular wind ONLY
• Quartering wind check never performed
• LeMessurier discovered bolts overstressed
• Emergency repair: 2" welded cover plates
Simulation Modules
Module 1: 3D Building Visualization
Module 2: ASCE 7-22 Wind Pressure
Module 3: 3D FEA (Direct Stiffness)
Module 4: AISC 360-22 Connections
Module 5: Monte Carlo Reliability
Module 6: Validation Summary
Module 10: 1978 vs Modern Comparison
Module 11: Data Provenance
Module 8-9: CFD Post-Processing (opt.)
Key Methods:
• ASCE 7-22 Ch. 27 (MWFRS)
• AISC 360-22 Eq. J3-3a (bolt interaction)
• Gumbel Type I (extreme wind)
• 100,000 Monte Carlo samples
• No circular reasoning in calibration
Sources: NIST (2021), Morgenstern (1995), ASCE 7-22, AISC 360-22 | Base MATLAB, no toolboxes

## Slide 2
Risk Analysis Results: Derived Failure Scenarios
All failure thresholds DERIVED from FEA + bolt capacity (not from historical data)
Scenario | V_fail (mph) | P_f (annual) | T_return (years) | Reliability Index β | Historical (LeMessurier)
1: Welded (perp.) | 180 | 7.5e-5 | 13,333 | 3.79 | N/A
2: Bolted (perp. only) | 106 | 1.3e-2 | 77 | 2.23 | N/A
3: Bolted, quart., NO TMD | 87 | 4.8e-2 | 21 | 1.67 | 70 mph / 16 yr
4: Bolted, quart., WITH TMD | 147 | 7.6e-4 | 1,318 | 3.17 | 85 mph / 55 yr
FEA & Connection Results
Nodes / Elements: 80 / 264
Max Disp. (perp.): 12.3 in
Max Disp. (quart.): 4.6 in
Drift Ratio: H/890
Equilibrium Error: 4.8e-15 (PASS)
Quartering Amp (FEA): 0.52x (< 1.0)
Historical Amp: 1.40x (static superposition)
NIST 2021 Finding: Face winds govern
D/C Ratios (AISC J3-3a)
Connection | Perp. | Quart. (FEA)
A325 Bolted (J3-3a) | 0.542 | 0.242
CJP Groove Weld | 0.308 | 0.161
Repaired (cover plates) | 0.268 | 0.140
Key Findings
Modern ASCE 7-22:
Quartering < perpendicular (amp=0.52). Face winds govern. Consistent with NIST 2021.
1978 Static Super.:
Quartering = 1.40x perpendicular. Overly conservative (static sum of correlated loads).
Bolt Crisis:
Real issue was bolts vs welds, regardless of wind angle. Bolts had insufficient capacity for any demanding scenario.
No Circular Logic:
Gumbel calibrated from ASCE 7 wind map. Failure V derived from FEA+bolts. Historical values for VALIDATION only.
Gumbel: μ=44.1, β=14.3 mph (from V₅₀=100, V₁₀₀=110) | 100,000 MC samples | FEA: 3D beam elements, direct stiffness