## Slide 1
Accurate NYC Building Meshes for CFD Simulation
Citicorp Center Wind Loading Analysis
OR 750 -- Reliability, Safety, and Risk
Data Sources | Methods | Validation

## Slide 2
Why Accurate Building Geometry Matters
CFD wind simulation requires realistic urban context
Wind loads on the Citicorp Center depend on surrounding buildings
  Upstream buildings create turbulence and wake effects
  Building blockage alters pressure distributions on target
  Missing or inaccurate neighbors = wrong wind loads
Our original mesh used 18 hand-estimated box buildings
  Approximate positions from Google Maps visual inspection
  Uniform flat-top extrusions (no roof shapes)
  Only ~276 triangles for surroundings geometry
Goal: Replace with surveyed NYC building data

## Slide 3
NYC Building Data Sources
Three levels of detail available
Source | Date | Detail | Format | Status
NYC Building Footprints (Socrata API) | Continuously updated | LoD1: footprint + roof height | GeoJSON (2D polygon + height) | Used as fallback
NYC 3D Building Model (CityGML) | Aug 2014 aerial survey | LoD1-2: actual roof/wall surfaces | CityGML XML (3D polygons) | Primary source
NYC 2017 Lidar (Topobathymetric) | May 2017 | Raw point cloud (8 pts/m^2) | LAS 1.4 (classified) | Available (not used)
Decision: CityGML provides the best balance of accuracy and usability. Actual roof shapes and wall setbacks without point cloud processing. Socrata API fills the gap for buildings constructed after 2014.

## Slide 4
LoD1 vs LoD2: What's the Difference?
Level of Detail in 3D city models
LoD1 -- Extruded Footprint
2D polygon extruded to a single height
Flat roof (no shape detail)
No setbacks or terracing
Good for distant buildings
Source: Socrata API (height_roof field)
LoD2 -- Surface Model
Actual WallSurface polygons at multiple Z
RoofSurface with slopes and ridges
GroundSurface at surveyed elevation
Captures setbacks, terraces, crowns
Source: CityGML (2014 aerial photogrammetry)
Example: Citicorp tower -- LoD1 = 12 triangles (flat box), LoD2 = 124 triangles (17 Z levels, irregular crown). For surrounding buildings, LoD1 is acceptable (blockage dominates). For the target building, LoD2 provides aerodynamically meaningful detail.

## Slide 5
Hybrid Data Pipeline
CityGML primary + Socrata API fallback
Step 1: Stream through CityGML DA district files (~764 MB each)
  Line-by-line parser to avoid loading into memory
  Extract buildings whose coordinates fall in CFD domain
  Parse WallSurface, RoofSurface, GroundSurface polygons
Step 2: Query Socrata API for buildings in same domain
  Returns current building inventory with heights
  Match by BIN (Building Identification Number)
Step 3: Merge -- CityGML geometry where available, Socrata extrusion for rest
  Buildings in both sources: use CityGML (more accurate)
  Buildings only in Socrata (built after 2014): extrude footprint
  Citicorp tower + stilts: always use hand-crafted geometry

## Slide 6
Coordinate Systems & Transforms
Three coordinate systems in the pipeline
System | Units | Source | Transform
WGS84 (EPSG:4326) | Degrees (lat/lon) | Socrata API, user input | Equirectangular projection
NY State Plane (EPSG:2263) | US Survey Feet | CityGML building data | Linear scaling (1200/3937 m/ft)
Local Cartesian | Meters | STL output (OpenFOAM) | Origin at Citicorp Z=0 at ground
Key parameters: Citicorp Center: 40.7579N, 73.9690W EPSG:2263 reference: X = 992,506 ft, Y = 215,620 ft Ground elevation: 25.78 ft MSL (from CityGML GroundSurface) US Survey Foot: 1200/3937 m = 0.30480061 m (NOT 0.3048) Linear approximation accurate to ~1m within 10km of reference point. No pyproj or GDAL dependencies needed.

## Slide 7
Results: Old vs. Hybrid Mesh
Quantitative comparison of surrounding building geometry
Metric | Old (Socrata LoD1) | Hybrid (CityGML + Socrata) | Improvement
Buildings | ~170 (API) | 806 (599 CityGML + 207 Socrata) | 4.7x
Triangles | ~14,000 | 64,486 | 4.6x
Surface types | Flat-top extrusion only | Wall + Roof + Ground surfaces | LoD2
Roof detail | None (all flat) | Actual shapes for 599 buildings | Realistic
Data currency | Present-day only | 2014 CityGML + present-day fill | Complete
Coverage | Socrata: 74% of hybrid total | CityGML: 74% Socrata fallback: 26% | --
BIN matching: 499 Socrata buildings matched to CityGML and replaced with higher-quality geometry. 207 buildings only in Socrata (built after 2014) -- extruded as LoD1 fallback. 3 Citicorp complex BINs excluded (hand-crafted tower + stilts).

## Slide 8
Limitations of the Original Mesh
Why the hand-estimated geometry was insufficient
Only 18 buildings -- Midtown Manhattan has 800+ in the CFD domain
  Missing buildings = missing blockage = wrong wake patterns
Positions estimated from Google Maps satellite view
  Typical error: 10-50m in X/Y placement
  No ground truth for building heights
All buildings were axis-aligned rectangular boxes
  Real footprints are L-shaped, irregular, with setbacks
  All roofs flat -- real roofs have slopes and crowns
No temporal filtering capability
  Could not distinguish 1978 vs. 2024 skyline
  Critical for studying the original structural crisis
276 total triangles vs. 64,486 in the hybrid mesh

## Slide 9
Citicorp Tower: Simplified vs. LoD2
BIN 1036474 -- Individual Landmark, 60 floors, built 1978
Property | Simplified STL | CityGML LoD2 | Difference
Triangles | 19 (12 box + 7 crown) | 124 | +105 (6.5x)
X/Y span | 67.7 m (axis-aligned) | 64.4 m (true outline) | -3.3 m
Height | 244.2 m (stilt to crown) | 283.7 m (ground to crown) | +39.6 m
Z levels | 4 | 17 | +13 levels
Cross-section | Perfect 45-degree diamond | Irregular polygon with setbacks | More realistic
Crown | 3-level approximation | ~10 distinct Z levels (241-284 m) | Detailed terracing
Stilts | 4 axis-aligned boxes | Not in CityGML (hidden from aerial) | Keep hand-crafted
Note: CityGML height (283.7m) exceeds actual 279m because rooftop equipment was captured by the photogrammetric survey. Stilts are not visible in aerial imagery -- hand-crafted geometry is retained for all configurations.

## Slide 10
Filling the Post-2014 Gap
Socrata fallback captures buildings missing from CityGML
NYC 3D Building Model is from 2014 aerial survey -- never updated
Notable buildings missing from CityGML near Citicorp:
Building | Distance | Height | Completed | CFD Impact
Selene (100 E 53rd) | ~50 m | 217 m (63 fl) | 2019 | HIGH
270 Park Ave (JPMorgan HQ) | ~600 m | 423 m (60 fl) | 2025 | MEDIUM
One Vanderbilt | ~1.2 km | 427 m (62 fl) | 2020 | LOW
Selene is the most critical missing building: at 217m and catty-corner to Citicorp, it significantly alters the local wind field. The Socrata API provides current building inventory. 207 post-2014 buildings were added via the fallback pipeline, including all buildings listed above.

## Slide 11
General-Purpose Extraction Tool
extract_buildings.py -- extract any NYC location
python extract_buildings.py --lat 40.7580 --lon -73.9690 --radius 300
Self-contained script: Python 3.8+ stdlib only (no pip installs)
Auto-detects DA district files, downloads from GitHub if missing
Streams through large GML files (~764 MB) line by line
Outputs: CityGML fragments + binary STL (OpenFOAM-ready)
Attributes extracted per building:
  BIN (Building Identification Number)
  Year built, number of floors, landmark status
  Height from roof/ground surface geometry
Tested: 31 buildings at Citicorp (100m radius), 4,392 triangles, ~40 seconds

## Slide 12
Technical Summary
What the hybrid pipeline provides
Capabilities
806 buildings in CFD domain
64,486 triangles (4.6x old mesh)
LoD2 surfaces for 74% of buildings
Present-day + historical (--year 1978)
BIN-based deduplication
Offline mode (CityGML only)
Hardcoded fallback (both fail)
Binary STL (OpenFOAM-ready)
Limitations
CityGML from 2014 (12 years old)
LoD2 detail only for ~100 iconic bldgs
Most CityGML buildings are LoD1
Fan triangulation (not ear-clipping)
No terrain elevation variation
Stilts not in aerial data
DA envelope matching too broad
Linear coord transform (~0.1% error)

## Slide 13
Next Steps
1. Run snappyHexMesh with hybrid geometry (target: 8-10M cells)
2. Compare drag coefficients:
  Old mesh (18 hand-estimated buildings) vs. hybrid (806 surveyed)
  Present-day skyline vs. 1978 skyline (--year 1978 filter)
3. Correct stilt geometry
  Rotate 45 degrees to match tower orientation
  Verify placement at face midpoints
4. Validate against published wind tunnel data
  Camelli et al. (2006) -- VLES of NYC wind fields
  ASCE 7-22 wind load provisions
5. ParaView visualization of building geometry comparisons